## Slide 1
Traffic Journey: Internet to Ashurst Offices
Internet
Start
Palo Alto
Front-Door Guard
Checks the envelope
Does NOT open it
FortiADC
Mailroom
Opens + reads the letter
App's Own Room
App VLAN
One room per app
FortiGate
Locked Office Door
Default answer = NO
Ashurst Offices
Corporate Network
End of the line
Exception App
Opens its own post
SD-WAN
EdgeConnect
Other sites
Main Line
Still sealed
Checked + clean
Needs internal data?
Only if on the list
Exception Line: passes through UNOPENED
FortiGate opens + inspects instead
Route control

## Slide 2
IoT_A VRF: Access Model
IoT_A VRF
Security Admin
via IoT_A jump box
CCURE Server
IoT_A
Corp VRF
Rapid 7 Engine
IoT_A
Door Panel
IoT_A, branch
Transition only
CCURE also manages legacy corporate-VLAN panels under time-bound exception
Manage cardholders / schedules
One-way vuln scan
Config + schedule push (port TBC) /
✕ Denied both ways

## Slide 3
Corp VRF / IoT_A VRF Segmentation
Corp VRF
Corporate Users / Servers / AD
IoT_A VRF (no corporate connectivity)
Branch Sites — IoT_A interfaces (blan1)
DC — IoT_A segment
Door Panels — Site A
802.1X MAC auth
Door Panels — Site B
802.1X MAC auth
Management Jump Box
(access method TBC)
CCURE Server
10.10.103.60
Identity Store
(IoT_A-local or exception — TBC)
Rapid 7 Scan Engine
(IoT_A)
Vendor update servers
(restricted egress TBC)
IoT BIO overlay
AES-GCM-256 tunnels
BMS_SECURITY zone
One-way scan
Direct breakout, not Netskope
✕ Denied both directions

## Slide 4
Current State: Flat Corporate VLAN
Office Site (Ashurst-owned)
Data Centre
Card Readers / Locks
Door Panel
Door Panel
CCTV Cameras / NVR
Corporate User PCs
Corporate VLAN
No IoT segregation
FW rules unknown
Lateral movement risk
Doors + CCTV + Corp share path
CCURE Server 10.10.103.90
Windows 2012 R2 (EOL)
CCURE Server 10.10.103.60
Like-for-like replacement
Physical Security Team
Direct login, no AD
Unencrypted / ad-hoc rules
Migration